## Slide 1: Guide to Networking Essentials, 9e
Chapter 3: Network Topologies and Technologies
.

## Slide 2: Chapter Objectives
By the end of this chapter, you should be able to:
Describe the primary physical networking topologies in common use
Describe the primary logical networking topologies in common use
Describe major LAN networking technologies
Compare Wi-Fi standards
Describe ring topology networks

## Slide 3: Physical Topologies
A network topology describes how a network is physically laid out and how signals travel from one device to another
  The physical layout of the devices and cables doesn’t describe how signals travel from one device to another
The arrangement of cabling and how cables connect one device to another in a network is considered the network’s physical topology
The path data travels between computers on a network is considered the network’s logical topology
  All network designs today are based on these basic physical topologies: bus, star, ring, and point-to-point

## Slide 4: Physical Bus Topology (1 of 3)
Physical bus topology is defined as a continuous length of cable connecting one computer to another in daisy-chain fashion
Weaknesses include the following:
  There’s a limit of 30 computers per cable segment
  The maximum total length of cabling is 185 meters
  Both ends of the bus must be terminated
  Any break in the bus brings down the entire network
  Adding or removing a machine brings down the entire network temporarily
  Maximum speed is 10 Mbps half-duplex communication

## Slide 5: Physical Bus Topology (2 of 3)
Figure 3-1 A physical bus topology network
This topology is now considered obsolete.

## Slide 6: Physical Bus Topology (3 of 3)
How Data Travels in a Physical Bus
  Electrical pulses (signals) travel the cable’s length in all directions
  Signals traveling across the medium and from device to device is called signal propagation
  The signal continues until it weakens or is absorbed by a terminator
  A terminator is an electrical component called a resistor that absorbs the signal instead of allowing it to bounce back up the wire
  If not terminated, the signal bounces or is “reflected” at end of medium, called signal bounce

## Slide 7: Physical Star Topology (1 of 5)
The physical star topology uses a central device (hub or switch) to connect computers
Advantages include the following:
  Much faster technologies than a bus
  Centralized monitoring and management of network traffic are possible
  Easier network upgrades
Using a central device allows for monitoring and managing a network
  When the number of workstations you need exceeds the number of ports on a central device you simply add another central device

## Slide 8: Physical Star Topology (2 of 5)
Figure 3-2 A physical star topology network

## Slide 9: Physical Star Topology (3 of 5)
The extended star topology is the most widely used in networks containing more than just a few computers
A central device (usually a switch) sits in the middle and instead of attached computers, other switches or hubs are connected to the central switch’s ports
  Computers and peripherals are attached to these switches or hubs forming additional stars
  Sometimes referred to as a “hierarchical star”
This topology is most effective when the center of the star is running at a much faster speed than other devices

## Slide 10: Physical Star Topology (4 of 5)
Figure 3-3 An extended star topology network

## Slide 11: Physical Star Topology (5 of 5)
Details of how data travels in a physical star depend on the central device
  The central device determines the ‘logical’ topology (discussed later)
    For now: hub = logical bus; switch = logical switching; MAU = logical ring (media access unit)
The main disadvantage is that the central device represents a single point of failure
  If the hub or switch fails or someone kicks the power cord out of the outlet, the entire network goes down

## Slide 12: Physical Ring Topology (1 of 2)
A physical ring topology is like a bus, in that devices are daisy-chained one to another
  Instead of terminating each end, the cabling is brought around from the last device back to the first device to form a ring
  This topology was most widely used to connect LANs with a technology called Fiber Distributed Data Interface (FDDI)
  FDDI was most often used as a network backbone, which is cabling used to communicate between LANs or between hubs and switches
Data travels in one direction

## Slide 13: Physical Ring Topology (2 of 2)
Figure 3-4 A physical ring topology is typically used to connect LANs

## Slide 14: Point-to-Point Topology (1 of 5)
A point-to-point topology is a direct link between two devices
Data travels on a dedicated link and bandwidth is not shared with other networks
Point-to-point technologies are used with wireless networks as a wireless bridge
  This setup can be used to connect two buildings without using a wired network
  It can also be used to connect two computers together for transferring files

## Slide 15: Point-to-Point Topology (2 of 5)
A point-to-multipoint (PMP) topology is an arrangement where a central device communicates with two or more other devices
  All communication goes through the central device
It is often used in WANs where a main office has connections to several branch offices via a router
A single connection is made from the router to a switching device that directs traffic to the correct branch office
A single base station communicates with multiple subscriber stations

## Slide 16: Point-to-Point Topology (3 of 5)
Figure 3-6 A point-to-multipoint topology

## Slide 17: Point-to-Point Topology (4 of 5)
A mesh topology connects each device to every other device in a network
  There are multiple point-to-point connections for the purposes of redundancy and fault tolerance
The purpose of creating a mesh topology is to ensure that if one or more connections fail, there’s another path for reaching all devices on the network
This topology is found in large WANs and internetworks
It is expensive due to additional cabling and ports required

## Slide 18: Point-to-Point Topology (5 of 5)
Figure 3-7 Switches in each building are connected in a full mesh topology

## Slide 19: Logical Topologies (1 of 3)
A network’s logical topology describes how data travels from computer to computer
  In some cases, it is the same as the physical topology
For a physical star, the central device determines the logical topology
A logical ring using a physical star implements the ring inside the central device’s electronics, which is a MAU in the token ring technology
In a switched topology, there is always an electrical connection between the computer and the switch

## Slide 20: Logical Topologies (2 of 3)
Figure 3-8 A logical bus implemented as a physical star
Figure 3-9 A logical ring implemented as a physical star

## Slide 21: Logical Topologies (3 of 3)
Figure 3-10 The logical functioning of a switch

## Slide 22: Knowledge Check Activity 3-1
What term describes how electricity behaves when it reaches the end of an unterminated cable?
a. Signal resistance
b. Signal propagation
c. Signal absorption
d. Signal bounce

## Slide 23: Knowledge Check Activity 3-1: Answer
What term describes how electricity behaves when it reaches the end of an unterminated cable?
Answer: d. Signal bounce
Explanation: The term used when electricity bounces off the end of a cable and back in the other direction is called signal bounce (or “reflection”). The traveling of data across the medium is called signal propagation. Signal absorption is when a signal is absorbed by a terminator device and resistance is a property of cabling that causes signal attenuation.

## Slide 24: Network Technologies
Network technology is the method a network interface uses to access the medium and send data frames and the structure of these frames
Other terms include the following:
  Network interface layer technologies, network architectures, and data link layer technologies
A network uses Ethernet, 802.11 wireless, or some combination of these to move data from device to device in your network
WAN examples include MPLS, SONET, and ATM (discussed in Chap. 10)
The network technology often defines frame format and media

## Slide 25: Network Technologies and Media (1 of 2)
Unshielded twisted pair (UTP) is the most common media type in LANs
  Consists of 4 pairs of copper wires, with each pair twisted together
  It comes in numbered categories
  The higher the number, the higher the cable’s bandwidth potential
Fiber-optic cabling uses thin strands of glass to carry pulses of light long distances and at high data rates
  It isn’t susceptible to electrical interference
  Can be used in electrically noisy environments

## Slide 26: Network Technologies and Media (2 of 2)
Coaxial cable is obsolete as a LAN medium but it is used as the network medium for Internet access via cable modem
Network technologies can use media to transmit signals in two main ways
  Baseband sends digital signals in which each bit of data is represented by a pulse of electricity or light
    Sent at a single fixed frequency and no other frames can be sent along with it
  Broadband uses analog techniques to encode binary 1s and 0s across a continuous range of values
    Signals flow at a particular frequency and each frequency represents a channel of data

## Slide 27: Ethernet Networks (1 of 8)
Ethernet is the most popular LAN technology
  Advantages include ease of installation, scalability, media support, and low cost
  It supports a broad range of speeds: 10 Mbps to 100 Gbps
Ethernet can operate in a physical bus or physical star and a bus or switched logical topology
Most NICs and switches can operate at multiple speeds: 10/100/1000
  The underlying technology is the same, regardless of speed

## Slide 28: Ethernet Networks (2 of 8)
Ethernet Addressing
  Every Ethernet station has a physical (MAC) address
  Each MAC address has 48 bits expressed as 12 hexadecimal digits
  Incoming frames are read for the destination MAC address and to see if they match the NIC’s own MAC address
  If they match or if the destination address is the broadcast MAC address, incoming frames are sent to the network protocol for further processing

## Slide 29: Ethernet Networks (3 of 8)
Ethernet Frames
  A frame is the unit of information that NICs and switches work with
  Frames must be between 64 and 1518 bytes and consist of the following:
  A 14-byte frame header composed of these three fields:
    Destination MAC (6 bytes)
    Source MAC (6 bytes)
    Type (2 bytes)
  A Data field from 45 to 1500 bytes
  A frame trailer (frame check sequence [FCS]) of 4 bytes

## Slide 30: Ethernet Networks (4 of 8)
Figure 3-12 Ethernet frame format

## Slide 31: Ethernet Networks (5 of 8)
Ethernet Media Access
  Media access method is a set of rules governing how and when the medium can be accessed for transmission
  Ethernet uses Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
    “Carrier sense” means to listen before send – must hear silence
    “Multiple access” means if two or more stations hear silence, multiple stations may transmit at the same time
  Collision detection: If two or more stations transmit, a collision occurs and is detected by the NIC; all stations must retransmit

## Slide 32: Ethernet Networks (6 of 8)
Figure 3-13 A network diagram showing two collision domains delimited by a switch
The extent to which signals in an Ethernet bus topology network are propagated is called a collision domain.

## Slide 33: Ethernet Networks (7 of 8)
Ethernet Error Handling
  Ethernet is a best-effort delivery system
    There’s no acknowledgement or verification that the frame arrived at its intended destination
    Ethernet relies on network protocols to ensure delivery
  Ethernet detects damaged frames
  The error-checking code in a frame’s trailer is called a Cyclic Redundancy Check (CRC)
    Ethernet uses the CRC to determine that data is unchanged
    If a frame is detected as damaged, it is discarded with no notification

## Slide 34: Ethernet Networks (8 of 8)
Half-Duplex versus Full-Duplex Communication
  Half-duplex works like a two-way radio; you can talk and listen but not both at the same time
  When hubs are used, NICs can only operate in half-duplex mode
  Full-duplex means NIC/switch can transmit/receive simultaneously
  CSMA/CD is not used because a collision cannot occur in full-duplex mode (Carrier Sense Multiple Access with Collision Detection)
  Full-duplex mode eliminates the delays caused by CSMA/CD and allows double the network bandwidth

## Slide 35: Ethernet Standards (1 of 4)
Ethernet standards expressed in one of two ways:
  Using the IEEE document number defining the standard (IEEE 802.3)
  XBaseY – 10BaseT, 100BaseT, 100BaseFX
    X – designates the speed of transmission
    Y – specifies the type of media (T = twisted-pair, FX = fiber optic)
10BaseT Ethernet
  Uses two of the four wire pairs and runs over Category 3 or higher UTP cabling
  It is highly susceptible to collisions and is obsolete
Part 2

## Slide 36: Ethernet Standards (2 of 4)
100BaseTX Ethernet is a common Ethernet variety
  It runs over Category 5e or higher UTP
  Uses two of four wire pairs
  Also sometimes called “Fast Ethernet”
100BaseFX Ethernet runs over two strands of fiber optic cabling
  It is typically used as backbone cabling between hubs or switches
  Also used to connect clients or servers when immunity to noise and eavesdropping is required

## Slide 37: Ethernet Standards (3 of 4)
1000BaseT Ethernet is usually called “Gigabit Ethernet”
  It runs over Category 5e or higher UTP and uses all four wire pairs
  To support full-duplex transmission over a single pair of wires:
    1000BaseT uses hybrid and canceller technology, which combines multiple signals and cancels interference
2.5GBaseT and 5GBaseT
  This specification was largely in response to increasing Wi-Fi speeds
  It runs over Cat 5e/6 cabling, so there is no need for a change in wiring infrastructure

## Slide 38: Ethernet Standards (4 of 4)
10GBaseT Ethernet runs over four pairs of Category 6A or 7 UTP
  It operates only in full-duplex mode
  No hubs, only switches support 10GBaseT
  It is still considered an expensive option, although prices are dropping
  Good for network servers so they can keep up with desktop systems that commonly operate at 1 Gbps
  The primary use of 10 Gigabit Ethernet technologies is as the network backbone

## Slide 39: Additional Ethernet Standards (1 of 3)
100BaseT4 uses all four pairs of wires in UTP Category 3 cable
  It is considered obsolete
1000BaseLX uses fiber-optic media
  “L” stands for “long wavelength” laser
  It supports a maximum cable segment length of 5000 meters
1000BaseSX uses fiber-optic media
  “S” stands for “short wavelength” laser, so it can’t cover as much distance as long-wavelength lasers, but they are less expensive

## Slide 40: Additional Ethernet Standards (2 of 3)
1000BaseCX uses specially shielded, balanced, copper jumper cables
  Might also be called “twinax” or “short-haul” copper cables
10 Gigabit Ethernet IEEE 802.3ae Standards are defined to run only on fiber-optic cabling and specifies a maximum distance of 40 kilometers
  It is primarily used for network backbones
  Varieties include 10GBaseSR, 10GBaseLR, 10GBaseER, 10GBaseSW, 10GBaseLW, and 10GBaseEW

## Slide 41: Additional Ethernet Standards (3 of 3)
40 and 100 Gigabit Ethernet switch ports are usually found as one or two uplink ports on switches
  Fiber optic cabling is primary medium, 40 Gbps is supported over Category 8 twisted-pair for up to 30 meters
25 and 50 Gigabit Ethernet most commonly use fiber optic cabling, 25 Gbps is available over Category 8 twisted-pair for up to 30 meters
In 2024, work began on 200, 400, and 800 Gbps Ethernet using 100 Gbps lanes and a task force to work on speeds up to 1.6 Terabits per second (Tbps) is scheduled for spring 2026

## Slide 42: 802.11 Wi-Fi
The 802.11 wireless networking standard is also referred to as Wireless Fidelity (Wi-Fi)
In most towns you can usually find a public Wi-Fi network, called a hotspot
802.11 is essentially an extension to Ethernet, using airwaves instead of cabling as the medium
802.11 networks can extend from several feet to several thousand feet

## Slide 43: Wi-Fi Modes of Operation
Wi-Fi can operate in one of the following modes:
  Infrastructure mode uses a central access point (AP)
    Stations connect through a wireless AP before they can communicate with other devices
  Ad hoc mode is a mode of operation where there is no central device
    Data travels from device to device like a bus and sometimes called “peer-to-peer mode”
Most of this chapter’s discussion of Wi-Fi focuses on infrastructure mode

## Slide 44: Wi-Fi Channels and Frequencies (1 of 2)
Wi-Fi networks operate at one of three radio frequencies: 2.4GHz, 5 GHz, and 6 GHz
  This frequency is not fixed
A wireless channel works like a TV channel:
  You must tune to the correct channel to connect
If you are configuring several Wi-Fi networks:
  Choose channels five apart from other known APs

## Slide 45: Wi-Fi Channels and Frequencies (2 of 2)
Figure 3-19 Selecting a Wi-Fi channel on an access point

## Slide 46: Wi-Fi Antennas
The antenna on a Wi-Fi device is both transmitter and receiver
Characteristics and placement determine how well a device transmits or receives Wi-Fi signals
Antennas are usually categorized by their radiation pattern:
  Omnidirectional antenna – the signal radiates out from the antenna with equal strength in all directions
  Unidirectional antenna – signals are focused in a single direction
    Ideal for placement at one end of long, narrow spaces

## Slide 47: Wi-Fi Access Methods and Operation
Wi-Fi devices use Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
  An acknowledgement is required for every packet sent
  802.11 standards specify a feature that uses handshaking before transmission
    Uses request-to-send/clear-to-send (RTS/CTS) packets and acknowledgements
The 802.11b standard specifies a transmission rate of 11 Mbps
  Environmental conditions can prevent transmission at this speed

## Slide 48: Wi-Fi Signal Characteristics (1 of 2)
Types of signal interference caused by physical objects include:
  Absorption — solid objects absorb radio signals, causing attenuation (weakening of the signal)
  Refraction — the bending of a radio signal as it passes from a medium of one density through a medium of a different density
  Diffraction — the altering of a wave as it tries to bend around an object
  Reflection — occurs when a signal hits a dense, reflective material, resulting in signal loss
  Scattering — when a signal changes direction in unpredictable ways, causing a loss in signal strength

## Slide 49: Wi-Fi Signal Characteristics (2 of 2)
Signal-to-noise ratio is the amount of noise compared with the signal strength
  Noise can come from equipment, other wireless devices, and other wireless networks
Throughput is the actual amount of data transferred, not counting errors and acknowledgements
Goodput is actual application-to-application data transfer speed
Extra megabytes in packet frame headers, acknowledgements, and retransmissions are collectively known as overhead

## Slide 50: Wi-Fi Standards (1 of 3)
Advantages and disadvantages of each standard:
  802.11b — was the most widely accepted standard because of its low cost and good indoor range
    Because it operates at only 11 Mbps, 802.11g and 802.11n have rapidly replaced it
  802.11a — requires more power and has a shorter indoor range, transfers data at 54 Mbps
  802.11g — suffers from the same interference problems as 802.11b networks
  802.11n — adds multiple-input/multiple-output (MIMO) antennas

## Slide 51: Wi-Fi Standards (2 of 3)
Advantages and disadvantages of each standard (continued):
  802.11ac — operates in the 5.0 GHz range only and can support data rates up to 1 Gbps
    Improves on the MIMO technology by providing up to eight data streams and introducing multiuser MIMO (MU-MIMO), which allows APs to send data to multiple client stations simultaneously
  802.11ax — known as Wi-Fi 6 and can provide speeds up to 9.6 Gbps using 160 MHz wide channels
    With this standard, the Wi-Fi Alliance introduced the new, simpler naming scheme, using numbers (Wi-Fi 5, Wi-Fi6, etc.)

## Slide 52: Wi-Fi Standards (3 of 3)
Advantages and disadvantages of each standard (continued):
  802.11be (Wi-Fi 7) — the newest adopted 802.11 standards that operates in the 2.4 GHz, 5 GHz, and 6 GHz bands
    In the 6 GHz band, it doubles the channel bandwidth to 320 MHz, allowing speeds up to 46 Gbps
  802.11bn (Wi-Fi 8) — the next iteration of the 802.11 standard
    It promises speeds up to 100 Gbps

## Slide 53: Wi-Fi Security
Signals from a Wi-Fi network can travel several hundred feet, so Wi-Fi devices outside your home or business can detect your signals
A Wi-Fi network should be protected by an encryption protocol that makes data difficult to interpret
Encryption protocols include Wired Equivalent Privacy (WEP), Wi-Fi Protected Access (WPA), and WPA2
  Not all devices support all three protocols
Wi-Fi encryption is configured on the AP

## Slide 54: Token Ring
Token ring is based on the IEEE 802.5 standard and are cabled in a star physical topology but function as a logical ring topology
  Originally operated at 4 Mbps and then increased to 16 Mbps and later 100 Mbps
  Uses cat 4 and higher UTP
  A token is passed along the network
  Only the station with the token can transmit
  Frames are acknowledged and token is released
  There are no collisions

## Slide 55: Fiber Distributed Data Interface Technology
Fiber Distributed Data Interface (FDDI) uses a token-passing access method and dual rings for redundancy
  The rings are usually a physical ring of fiber-optic cable
FDDI transmits at 100 Mbps and can include up to 500 nodes over a distance of 62 miles
  FDDI full-duplex technology can support up to 200 Mbps
Devices called “concentrators” can serve as a central connection point for buildings or sites in a campus setting
This technology is obsolete on new networks

## Slide 56: Knowledge Check Activity 3-2
Wi-Fi networks currently operate in which three frequencies?
a. 2.4 MHz, 5 MHz, 6 MHz
b. 2.4 GHz, 5 GHz, 6 GHz
c. 11 MHz, 54 MHz, 108 MHz
d. 11 GHz, 54 GHz, 108 GHz

## Slide 57: Knowledge Check Activity 3-2: Answer
Wi-Fi networks currently operate in which three frequencies?
Answer: b. 2.4 GHz, 5 GHz, 6 GHz
Explanation: While some of the Wi-Fi standards operate in either the 2.4 GHz or 5 GHz frequencies, some standards operate in both frequencies. The Wi-Fi 6e standard operates in the 2.4 GHz, 5 GHz, and 6GHz frequencies.

## Slide 58: Self Assessment
Name the differences between physical topology and logical topology.
You’re configuring a WLAN in a long, narrow ballroom. The only place you can put the AP is at the far end of the room. Which type of antenna should you use?

## Slide 59: Summary
Now that the lesson has ended, you should be able to:
Describe the primary physical networking topologies in common use
Describe the primary logical networking topologies in common use
Describe major LAN networking technologies
Compare Wi-Fi standards
Describe ring topology networks