## Slide 1: Guide to Networking Essentials, 9e
Chapter 4: Network Media
.

## Slide 2: Chapter Objectives
By the end of this chapter, you should be able to:
Define the primary cable types used in copper network cabling
Describe the characteristics of the major types of fiber-optic network cabling
Explain the technologies used for wireless networking
Select the proper media for a given application

## Slide 3: Criteria for Choosing Network Media (1 of 5)
Bandwidth Rating
  Bandwidth is the number of bits per second that can be transmitted across a medium
  A factor determining bandwidth is how bit signals are represented on the medium (called encoding)
  When possible, choose a cabling category that’s compatible with the standard you want to implement now but will support growth and faster speeds

## Slide 4: Criteria for Choosing Network Media (2 of 5)
Maximum Segment Length
  A cable segment is a length of cable between two network devices
  Intermediate passive devices, such as wall jacks, are considered part of the total segment length
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)

## Slide 5: Criteria for Choosing Network Media (3 of 5)
Interference to electrical signals on copper media comes in the form of electromagnetic interference (EMI) and radio frequency interference (RFI)
  Motors, transformers, fluorescent lights and other sources of intense electrical activity can emit both EMI and RFI.
  RFI can also affect wireless networks
  Crosstalk is interference one wire generates on another wire when both wires are in a bundle
  Copper wire is susceptible to electronic eavesdropping
  Fiber-optic media carries light signals and is not susceptible to EMI

## Slide 6: Criteria for Choosing Network Media (4 of 5)
Cable Grade
  Cables ran between a false ceiling and the true ceiling (plenum) must be plenum-rated
  UTP cabling is marked as communications riser (CMR) or communications plenum (CMP)
  CMR can only be used for building risers or in cable trays and CMP is suitable for use in plenum spaces
Connection Hardware
  Every type of cable has connectors that influence the kinds of hardware the cable can connect to

## Slide 7: Criteria for Choosing Network Media (5 of 5)
Other Media Considerations
  Ease of installation
  Testability
  Total cost

## Slide 8: Coaxial and Twinax Cable
Coaxial cable is often called “coax” for short
  It is inexpensive and easy to install, but started to phase out in the early 1990’s
Today, coaxial cable is used primarily in connecting a cable modem to the wall outlet your cable TV/Internet provider installs
Twinax cable is used in high-speed connections over short distances
  It can support Ethernet speeds up to 100 Gbps at a maximum distance of 15 meters
  Used in datacenters connecting storage devices and servers to switches

## Slide 9: Twisted-Pair Cable (1 of 9)
Twisted-pair (TP) cable comes in two types: unshielded and shielded (UTP and STP)
TP consists of one or more pairs of insulated strands of copper wires twisted around one another and housed in an outer jacket
  Twists are necessary to improve resistance to crosstalk from wires and EMI from outside sources
  The more twists per unit length, the better resistance to EMI and crosstalk
More expensive TP is twisted more than less expensive and provides a better pathway for higher bandwidth networks

## Slide 10: Twisted-Pair Cable (2 of 9)
Figure 4-1 STP and UTP cable

## Slide 11: Twisted-Pair Cable (3 of 9)
Unshielded Twisted-Pair Cable consists of four pairs of insulated wires
It is rated according to categories devised by the Telecommunications Industry Association (TIA) and Electronic Industries Alliance (EIA) and American National Standards Institutes (ANSI)
Categories 1-6a and Category 8 are accepted in US
  Two additional categories aren’t yet TIA/EIA standards
  Europe has accepted Category 7 and 7a, which specify that each wire pair is shielded
Categories 5e and 6 are the most installed categories of UTP cabling

## Slide 12: Twisted-Pair Cable (4 of 9)
Characteristic | Value
Maximum cable length | 100 m (328 ft)
Bandwidth | Up to 1000 Mbps
Bend radius | Minimum four times the cable diameter of 1 inch
Installation and maintenance | Easy to install, no need to reroute; the most flexible
Cost | Least expensive of all cabling options
Connector type | RJ-45 plug, RJ-45 jack, and patch panels
Security | Moderately susceptible to eavesdropping
Interference rating | Susceptible to EMI and crosstalk
Table 4-1 Category 5e and 6 UTP cabling characteristics

## Slide 13: Twisted-Pair Cable (5 of 9)
Shielded Twisted-Pair (STP) cable includes shielding to reduce crosstalk and interference
STP has a wire braid inside the sheath material or a foil wrap
It is best to use STP in electrically noisy environments or for very high-bandwidth applications
Common STP versions found in networks today include Cat 5e, Cat 6, and Cat 6a
STP is sometimes referred to as “foiled twisted pair (FTP)”

## Slide 14: Twisted-Pair Cable (6 of 9)
Twisted-Pair Cable Plant Components
  RJ-45 Connectors—most STP and UTP cabling uses RJ-45 connectors (RJ-45 plug) to connect computers to hubs, switches, and RJ-45 jacks
  Patch cable—a short cable for connecting a computer to an RJ-45 wall jack or connecting a patch-panel port to a switch or hub
  RJ-45 jacks—an RJ-45 jack is what you plug an RJ-45 connector into when the computer is in a work area away from hubs and switches
    RJ-45 jacks are usually placed behind wall plates when cables are run inside walls but can be recessed into the floor or placed in surface-mounted boxes

## Slide 15: Twisted-Pair Cable (7 of 9)
Twisted-Pair Cable Plant Components
  Patch Panels—used to terminate long runs of cable from where the computers are to the wiring closet (where the switches and hubs are)
  Distribution racks—hold network equipment such as routers and switches, plus patch panels and rack-mounted servers
    Also called 19” racks because the upright rails are 19” apart

## Slide 16: Twisted-Pair Cable (8 of 9)
Figure 4-3 An RJ-45 plug
Figure 4-5 An RJ-45 jack

## Slide 17: Twisted-Pair Cable (9 of 9)
Figure 4-6 Patch panel front and back
Figure 4-7 A distribution rack

## Slide 18: Structured Cabling: Managing and Installing a UTP Cable Plant (1 of 12)
Structured cabling specifies how cabling should be organized, regardless of the media type or network architecture
Large networks typically use most or all of these components:
  Work area
  Horizontal wiring
  Telecommunication closets
  Equipment rooms
  Backbone or vertical wiring
  Entrance facilities

## Slide 19: Structured Cabling: Managing and Installing a UTP Cable Plant (2 of 12)
The work area is where workstations and other user devices are located
  Faceplates and wall jacks are installed in the work area and patch cables connect computers and printers to wall jacks
Horizontal wiring runs from the work area’s wall jack to the telecommunication closet
  Wiring from the wall jack to the patch panel should be no longer than 90 meters (plus 10 meters for patch cables)

## Slide 20: Structured Cabling: Managing and Installing a UTP Cable Plant (3 of 12)
Figure 4-8 Work area components

## Slide 21: Structured Cabling: Managing and Installing a UTP Cable Plant (4 of 12)
The telecommunications closet (TC) provides connectivity to computer equipment in the nearby work area
  A TC that houses the cabling and devices for work area computers is referred to as an intermediate distribution frame (IDF)
The equipment room houses servers, routers, switches, and other major network equipment and serves as a connection point for backbone cabling
  An equipment room that’s the connection point between IDFs is called a main distribution frame (MDF) or “main cross-connect”

## Slide 22: Structured Cabling: Managing and Installing a UTP Cable Plant (5 of 12)
Backbone cabling interconnects IDFs and MDFs
  This cabling runs between floors or wings of a building and between buildings
  It is often fiber-optic cable but can also be UTP if the distance between TCs is less than 90 meters
Entrance Facility is the location of the cabling and equipment that connects a corporate network to a third-party telecommunications provider
  It can also serve as an equipment room and the main cross-connect for all backbone cabling

## Slide 23: Structured Cabling: Managing and Installing a UTP Cable Plant (6 of 12)
Figure 4-10 Backbone cabling connecting IDFs and MDFs

## Slide 24: Structured Cabling: Managing and Installing a UTP Cable Plant (7 of 12)
Installing UTP Cabling
  Cable termination means putting RJ-45 plugs on the ends of cable or punching down wires into terminal blocks on a jack or patch panel
  When making a cable or terminating a cable at a jack or patch panel it is important to get the colored wires arranged in the correct order
  There are two standards: TIA/EIA 568A and TIA/EIA 568B (see Figure 4-12 on the following slide)

## Slide 25: Structured Cabling: Managing and Installing a UTP Cable Plant (8 of 12)
Figure 4-11 Cable installation and termination tools

## Slide 26: Structured Cabling: Managing and Installing a UTP Cable Plant (9 of 12)
Standard patch cables are called straight-through cables (same wiring standard on both ends)
Crossover cables use 568A standard on one side of the cable and 568B standard on the other side
  This type of cable crosses the transmit and receive wires so that transmit on one end connects to receive on the other
  This type of cable is often needed when you connect two devices of the same type to one another
  For a 1000BaseT crossover cable, you have to cross the blue and brown pins because they’re used in 1000BaseT

## Slide 27: Structured Cabling: Managing and Installing a UTP Cable Plant (10 of 12)
Figure 4-12 TIA/EIA 568A and 568B cable pinouts

## Slide 28: Structured Cabling: Managing and Installing a UTP Cable Plant (11 of 12)
Network devices connecting with RJ-45 plugs are classified as medium dependent interface (MDI) devices or MDI crossed (MDI-X) devices
  MDI devices transmit on pins 1 and 2 and receive on pins 3 and 6
  MDI-X devices receive on pins 1 and 2 and transmit on pins 3 and 6
    Usually hubs and switches are examples
When two switches need to be connected, you use a crossover cable so that transmit and receive wires get crossed
  Some devices have “auto-sensing” (Auto-MDI-X) ports that can detect whether you are trying to connect transmit wires to transmit wires

## Slide 29: Structured Cabling: Managing and Installing a UTP Cable Plant (12 of 12)
Why Two Transmit and Two Receive Wires?
  One wire pair is used for transmit (labeled transmit+/transmit-) and one pair for receive (labeled receive+/receive-)
  The plus and minus symbols indicate that the wires carry a positive or a negative signal
  This differential signal mitigates the effect of crosstalk and noise on the cable
https://www.yout-ube.com/watch?v=gzVe_GnbifI Fiber - copper

## Slide 30: Knowledge Check Activity 4-1
To support 1000BaseT Ethernet, what is the minimum cabling category you should use?
a. Category 4
b. Category 5e
c. Category 6a
d. Category 7
Part 2

## Slide 31: Knowledge Check Activity 4-1: Answer
To support 1000BaseT Ethernet, what is the minimum cabling category you should use?
Answer: b. Category 5e
Explanation: Category 5 cabling can be used in Gigabit Ethernet (1000BaseT), but Cat 5e is the minimum recommendation because of the additional tests required for it.

## Slide 32: Fiber-Optic Network Cabling
With fiber-optic cable, bits are transmitted as pulses of light instead of electricity
  Makes it immune to electrical interference and eavesdropping
Composition of fiber-optic cable:
  A slender cylinder of glass fiber called the core is surrounded by a concentric layer of glass called the cladding
  Fiber is then jacketed in a thin transparent plastic material called the buffer
  In most cases, each fiber-optic strand carries data in only one direction

## Slide 33: Fiber-Optic Connectors (1 of 2)
Types of fiber-optic connectors include the following:
  Straight tip (ST)
  Straight connection (SC)
  Locking connection (LC)
  Mechanical transfer registered jack (MT-RJ)
  Fiber channel or ferrule connector (FC)
  Medium interface connector (MIC)
  Subminiature type A (SMA)

## Slide 34: Fiber-Optic Connectors (2 of 2)
Figure 4-19 Fiber-optic connectors

## Slide 35: Fiber-Optic Installation
Installing fiber-optic networks is more difficult than installing copper media
  However, advances in connector technology are closing the gap
  Connectors and test equipment required for termination are still more expensive than copper
There are many methods for terminating fiber-optic cables because of the many connectors and cable types available
Installation details are beyond the scope of this book

## Slide 36: Fiber-Optic Cable Types
Single-mode fiber (SMF):
  Includes a single, small-diameter fiber at the core (8 microns)
  Works with laser-based emitters and spans the longest distances
  Used in higher-bandwidth applications
Multimode fiber (MMF) :
  Larger diameter fiber at the core (50 and 62.5 microns) and costs less than SMF
  Works with lower-power light emitting diodes (LEDs)
  Spans shorter distances

## Slide 37: Cable-Testing Equipment
Common tools for testing and troubleshooting wired networks:
  Cable certifier
  Basic cable tester
  Tone generator
  Time domain reflectometer (TDR)
  Multimeter
  Optical power meter (OPM)

## Slide 38: Wireless Networking
Wireless networks are often used with wired networks to interconnect geographically dispersed LANs or groups of mobile users with wired servers and resources on a wired LAN
Even in small networks with workstations connecting to a wireless AP or router, the AP or router usually connects to the Internet via a wired connection to a cable modem

## Slide 39: Wireless Benefits (1 of 2)
Wireless networking can offer the following capabilities:
  Create temporary connections to wired networks
  Establish backup or contingency connectivity for existing wired networks
  Extend a network’s span beyond the reach of wire-based or fiber-optic cabling, especially in older buildings where rewiring might be expensive
  Allow businesses to provide customers with wireless networking easily, offering a service that gets customers in and keeps them there
  Enable users to roam around an organization or college campus with their devices

## Slide 40: Wireless Benefits (2 of 2)
Figure 4-20 A typical home wireless network

## Slide 41: Types of Wireless Networks
Wireless networks can be subdivided into the following categories:
  Local area networks (LANs)—usually provides connectivity for mobile users or across areas that couldn’t otherwise be networked
  Extended LANs—usually used to increase a LAN’s span beyond normal distance limitations
  Internet service—used to bring Internet access to homes and businesses
  Mobile computing—users communicate by using a wireless networking medium which enables them to move while remaining connected to a network

## Slide 42: Wireless LAN Components
A network interface includes an antenna, which converts outgoing digital signals into radio waves and vice versa
An access point (AP) includes an antenna and a transmitter/receiver device to send and receive wireless traffic
  It also connects to the wired side of the network
  This connection enables the device to move network data back and forth between a network’s wired and wireless sides

## Slide 43: Wireless LAN Transmission (1 of 2)
Wireless communications depends on sending and receiving signals broadcast through the air to carry information
These signals take the form of radio waves in the electromagnetic (EM) spectrum
The frequency of the wave forms used for communication is measured in cycles per second, usually expressed as hertz (Hz)
Lower-frequency transmissions can carry less data more slowly over longer distances, and higher-frequency transmissions can carry more data faster over shorter distances

## Slide 44: Wireless LAN Transmission (2 of 2)
The following are common frequencies for wireless communication:
  Traditional radio—10 KHz to 300 MHz
  Microwave—300 MHz to 300 GHz
  Infrared—300 GHz to 400 THz (terahertz)
Higher frequency signals have higher bandwidth potential, but travel shorter distances and have a harder time traveling through obstacles
Lower frequency signals have lower bandwidth potential, but travel longer distances and travel better through obstacles

## Slide 45: LAN Media Selection Criteria (1 of 3)
When choosing between media types, consider:
  Bandwidth—Higher bandwidth means more expensive cable and higher installation costs
  Budget—A typical UTP cable installation cost $100-$200 per cable run and fiber-optic might cost twice that much
  Environmental considerations—How electrically noisy is the environment? How important is data security?

## Slide 46: LAN Media Selection Criteria (2 of 3)
When choosing between media types, consider (continued):
  Span—What kind of distance must the network span?
    Longer spans might require fiber-optic or wireless be used between buildings
  Existing cable plant—For an upgrade, the existing cable plant must be considered

## Slide 47: LAN Media Selection Criteria (3 of 3)
Type | Maximum cable length | Bandwidth | Installation | Interference | Cost
UTP | 100 m | 10-10,000 Mbps | Easy | High | Cheapest
STP | 100 m | 16-10,000 Mbps | Moderate | Moderate | Moderate
Fiber optic | 2-100 km | 100 Mbps – 100 Gbps | Moderate | None | Most expensive
Wireless | 100-300 feet | 11 Mbps – 46 Gbps | Easy | Moderate | Moderate for APs, none for physical media
Table 4-5 Comparison of LAN media characteristics

## Slide 48: Knowledge Check Activity 4-2
Under which circumstance should only fiber-optic cabling be used for Ethernet applications?
a. 90-meter cable segment running at 10 Gbps
b. Any connection speed over 1 Gbps
c. 200-meter cable segment running at 1 Gbps
d. All 10 Gbps connections

## Slide 49: Knowledge Check Activity 4-2: Answer
Under which circumstance should only fiber-optic cabling be used for Ethernet applications?
Answer: c. 200-meter cable segment running at 1 Gbps
Explanation: Since copper cable segments have a maximum length of 100 meters, any segments longer than 100 meters should use fiber-optic cabling.

## Slide 50: Self Assessment
Name some examples of where using fiber-optic cabling would be a better choice over using twisted-pair cabling.
When would you need to use a crossover cable as opposed to a straight-through cable?

## Slide 51: Summary
Now that the lesson has ended, you should be able to:
Define the primary cable types used in copper network cabling
Describe the characteristics of the major types of fiber-optic network cabling
Explain the technologies used for wireless networking
Select the proper media for a given application
https://www.yout-ube.com/watch?v=P_188oMgfuQ
Home Network …