## Slide 1: Guide to Networking Essentials, 9e
Chapter 13: The Internet of Things (IoT)
.

## Slide 2: Chapter Objectives
By the end of this chapter, you should be able to:
Define the Internet of Things and list use cases
Describe IoT network technologies
Discuss a variety of IoT devices
Utilize DIY IoT devices

## Slide 3: Introduction to the Internet of Things
The Internet of Things (IoT) is the digitization of items through the use of networked microprocessors and microcontrollers along with sensors, actuators, motors, and other I/O devices, plus software
Examples of IoT:
  Amazon Echo or Google Assistant
  Smoke detectors, motion sensors, and intelligent thermostats
  Water pumps
Between 17 and 18 billion IoT devices are estimated to be connected to the Internet in 2024
youtube.com/watch?v=81GdhsfDnsg

## Slide 4: IoT Use Cases (1 of 3)
IoT and Transportation
  Google uses location, speed, and direction information provided by smartphones being used on roads to detect traffic jams or accidents
  Self-driving cars are filled with sensors, communication devices, and microprocessors
IoT and Energy
  Utility usage patterns can be used to determine peak usage periods and even detect leaks or illegal activity
  IoT is being used to improve operator safety in mining for energy products such as coal and natural gas

## Slide 5: IoT Use Cases (2 of 3)
IoT and Manufacturing
  The majority of machines used in manufacturing are not connected to a network, but most would benefit from such a connection
  IoT can be used to monitor the status of equipment and detect potential problem indicators such as excessive heat build-up, excessive vibration, or too many operation cycles between standard and maintenance tasks
  Data-driven manufacturing reduces waste in material goods and energy

## Slide 6: IoT Use Cases (3 of 3)
IoT and Emergency Services
  IoT can be used to locate victims
  Wearable fitness devices could monitor respiration, blood pressure, temperature, and other vital signs and could be sent to a mobile diagnostic device carried by a first responder
  Emergency responders may also carry specialized sensors to collect data from the environment and the victim
  Robots are being used to investigate dangerous environments such as collapsed buildings or mine shafts, and to investigate suspicious objects that could contain explosives

## Slide 7: IoT Technologies (1 of 3)
The goals of most IoT technologies are to collect, process, analyze, react to, and communicate data
  Any technology that does one or more of those tasks is a candidate for use in IoT applications
IoT Data Collection
  Common types of sensors used in IoT include:
    Audio sensors, proximity sensors, light sensors, accelerometers and gyroscopes, temperature and humidity sensors, motion and occupancy sensors, biometric sensors

## Slide 8: IoT Technologies (2 of 3)
IoT Data Processing
  IoT data processing occurs in two places:
    The front end, where the sensors collect the data are located; this is often referred to as edge processing or edge computing
    The back end, a central location where data is usually sent via a network connection
  A microcontroller is a small, low-power processor with built-in analog and digital I/O lines and memory that usually runs at speeds measured in the tens of Megahertz
    A microcontroller is usually at the heart of an embedded system, a computing system designed to perform a specific function

## Slide 9: IoT Technologies (3 of 3)
IoT Data Communication
  Various consortiums are in the process of developing standards for IoT communications
  The communication aspect of IoT is complex because so many of the “things” that generate data are incompatible with one another or lack modern communication technologies and protocols
youtube.com/watch?v=w0bZrOG9WR0
Data – Deception IoT

## Slide 10: IoT Networking (1 of 2)
Different types of devices and different environments dictate what type of networking technology is likely to be used by a particular IoT device
Many IoT devices use some form of wireless communication
The network technology used by an IoT device largely depends on the following factors:
  Distance
  Bandwidth
  Power consumption

## Slide 11: IoT Networking (2 of 2)
Primary IoT area network types and some of the technologies they are likely to use include the following:
  Neighborhood area network (NAN)—primarily used in the utility industry to wirelessly collect data from utility meters
    A similar network type, a field area network (FAN), is also used in utility applications and works with NAN technologies
  Local area network (LAN)—IoT devices use the same LAN technologies that any connected computing device might use
  Personal area network (PAN)—PANs use short-range network technologies such as 802.15 Bluetooth

## Slide 12: IoT Networking Technologies Overview (1 of 3)
Wired technologies are sometimes used in IoT—however, wireless dominates the field in most applications
  802.11 Wi-Fi—IoT devices can use one of the 802.11 Wi-Fi LAN standards if the bandwidth requirements are high and power is plentiful
  Bluetooth—There are IoT-specific revisions to the Bluetooth standard (Bluetooth 4.2 and 5.0)
    Bluetooth 6.0 includes improved distance measurement between devices for enhanced security and other improved reliability features
  Zigbee, 6LoWPAN, and Thread—These technologies are based on IEEE 802.15.4, which specifies low-bandwidth, low-power, and inexpensive devices

## Slide 13: IoT Networking Technologies Overview (2 of 3)
Figure 13-2 A Zigbee-enabled smart lock

## Slide 14: IoT Networking Technologies Overview (3 of 3)
Wired technologies are sometimes used in IoT—however, wireless dominates the field in most applications (continued)
  Z-Wave—is used primarily in home automation to wirelessly connect smart devices such as locks, thermostats, lighting, and security systems
    It is a wireless mesh technology that allows devices to communicate with one another and with a central control hub that serves as a gateway to the home Wi-Fi network so devices can be controlled with smart home assistants and smartphones
  LoRaWAN—is a low-power wide-area network technology that operates over a wide range of frequencies under 1 GHz

## Slide 15: Knowledge Check Activity 13-1
Which type of network might be used to collect data from a consumer utility meter?
a. NAN
b. WAN
c. FAN
d. MAN

## Slide 16: Knowledge Check Activity 13-1: Answer
Which type of network might be used to collect data from a consumer utility meter?
Answer: a. NAN
Explanation: Neighborhood area networks (NANs) are primarily used in the utility industry to wirelessly collect data from utility meters. NAN technologies can reach distances of dozens of kilometers and have low bandwidth requirements. A similar network type, a field area network (FAN), is also used in utility applications and works with NAN technologies. Whereas NAN technologies connect from the consumer endpoint to the utility network, FAN technologies connect utility network nodes with one another.

## Slide 17: Home Automation and Industrial IoT Devices
Industrial IoT (IIoT) uses some of the same technologies as other IoT devices but differs in many aspects, such as security, ruggedness, networking, and the types of devices involved
IIoT is used in utilities, energy, healthcare, manufacturing, city infrastructure, and other industries
This section introduces you to common IoT devices and use cases from both commercial and industrial sectors of IoT

## Slide 18: A Sampler of Home Automation IoT Devices (1 of 3)
Popular IoT devices used in the home and office include:
  Smart home assistants
  Smart thermostats, smart vents, smart light bulbs, smart door locks
  Video doorbells
  Smoke alarms
  Garage door openers and security systems
  Irrigation systems
  Smart appliances

## Slide 19: A Sampler of Home Automation IoT Devices (2 of 3)
Figure 13-3 Amazon Echo
Figure 13-4 Google Home

## Slide 20: A Sampler of Home Automation IoT Devices (3 of 3)
Figure 13-5 ecobee smart thermostat

## Slide 21: Industrial IoT Devices (1 of 6)
The use of IoT technologies in industry has been dubbed Industry 4.0
Industry 4.0 makes use of virtualization, cloud computing, and artificial intelligence to create what is called a cyber-physical system (CPS)
Some of the same IoT technologies are used in both home automation and industry
Industrial usage often requires industrial versions of sensors because they must hold up under harsh environments, high vibrations, and possibly extreme temperatures

## Slide 22: Industrial IoT Devices (2 of 6)
Figure 13-7 An industrial IoT wireless vibration sensor

## Slide 23: Industrial IoT Devices (3 of 6)
Types of devices you might find in industrial applications include the following:
  Actuators—a general category of output device that provides automatic movement, such as turning a valve to open or close a pipe
  Electric motor—rotates at a particular speed and direction in response to an electrical signal
    Stepper motors rotate in a series of steps, providing precise movement
    Servo motors provide either partial rotation or continuous rotation
  Solenoid—a tightly wound coil of wire that creates a strong magnetic field when electricity is applied

## Slide 24: Industrial IoT Devices (4 of 6)
Figure 13-8 A servo motor

## Slide 25: Industrial IoT Devices (5 of 6)
Types of devices you might find in industrial applications include the following (continued):
  RFID tags—attached to objects and are used to identify and track the objects
  PLCs—programmable logic controllers (PLCs) are input/output controllers used in assembly lines, robotics, and automated machinery
  IoT gateways—devices that translate data coming from an IoT network to another type of network
youtube.com/watch?v=wCycn_4VEe4
Buildings & IoT – friends?

## Slide 26: Industrial IoT Devices (6 of 6)
Figure 13-9 An IoT-enabled PLC

## Slide 27: DIY IoT (1 of 3)
Examples of DIY IoT:
  Studying changes in rock density due to atmospheric conditions
  Measuring how many hours of direct sunlight your plants are getting
  Creating a wildlife detection and alarm system
Part 2
youtube.com/watch?v=dVG8W-0p6vg
Tech Promised Everything. Did it deliver? - July 2025

## Slide 28: DIY IoT (2 of 3)
Figure 13-10 A sunlight detection IoT device

## Slide 29: DIY IoT (3 of 3)
Figure 13-11 A wildlife detection and alarm IoT device

## Slide 30: Getting Started with IoT (1 of 6)
Companies that cater to the DIY crowd:
  Sparkfun—www.sparkfun.com
  Adafruit—www.adafruit.com
Sparkfun partners with educational institutions to offer webinars, curricula, instructor training, and lab kits
Tinkercad from Autodesk allows you to start experimenting with IoT without any investment in hardware or equipment by using an online circuit simulator

## Slide 31: Getting Started with IoT (2 of 6)
Figure 13-12 A circuit in Tinkercad

## Slide 32: Getting Started with IoT (3 of 6)
The following is a list of items you’ll likely need to get started with IoT:
  Microcontroller development board
  Solderless breadboard—a development tool into which you plug components, giving you access to the computer’s input and output lines
  Sensors—common sensors include LDRs, PIRs, temperature sensors, accelerometers, infrared receivers, force sensors, and audio sensors
  LEDs—light-emitting diodes (LEDs) are small electronic devices that emit light when an electrical current is applied
    LEDs are used as indicator lights

## Slide 33: Getting Started with IoT (4 of 6)
Figure 13-13 An Arduino Uno

## Slide 34: Getting Started with IoT (5 of 6)
The following is a list of items you’ll likely need to get started with IoT (continued):
  Actuators
  Display components
  Passive components – such as resistors, capacitors, and diodes are part of most electronic designs
  Power supply
  Jumper wire - a short length of insulated wire that has a pin or socket on each end and is used to conduct electricity from one component to another

## Slide 35: Getting Started with IoT (6 of 6)
Figure 13-15 Jumper wire

## Slide 36: Tools for IoT
You will likely need some basic tools during the development process:
  Wire cutters
  Soldering iron
  Digital voltmeter
  Helping hands—a tool with alligator clips on the end of articulating arms that hold things in place

## Slide 37: IoT Software Development (1 of 6)
Most microcontroller development boards have an associated integrated development environment (IDE)
  An IDE allows you to write, edit, debug, and prepare programs for upload to the development board for execution by the microcontroller
  This chapter focuses on the Arduino IDE, which is designed specifically for writing programs for Arduino and Arduino-compatible development boards
  You write programs in the Arduino IDE using the C and C++ languages
  The IDE has downloadable libraries to support sensors, actuators, network interfaces, and other I/O devices

## Slide 38: IoT Software Development (2 of 6)
An Arduino program is called a sketch
When you start a new one, the IDE fills in the basic structure that all sketches use:
  setup()—When you download an Arduino sketch, the microcontroller begins by executing the code in the setup() section
    This section is used to initialize devices and perform other tasks that should only be executed once for the duration of the program
  loop()—The loop section is where the main program code resides

## Slide 39: IoT Software Development (3 of 6)
Figure 13-17 An Arduino program that blinks an LED

## Slide 40: IoT Software Development (4 of 6)
IoT Development with Python
  There are variations of Python for microcontrollers, including MicroPython and CircuitPython
  Development boards that support Python have more flash and RAM and usually run at higher clock rates than those that are meant to support only the Arduino environment
  Python is an interpreted language and the interpreter uses flash and RAM on the development board

## Slide 41: IoT Software Development (5 of 6)
IoT with Raspberry Pi
  The Raspberry Pi 3 is a full-featured personal computer on a single board the size of a credit card
  It has a quad-core, 1.4 GHz processor and was designed for more complex tasks
  It runs the Linux OS, a distribution called Raspbian, and has Python built in
  It is best suited for running computing-intensive applications, collecting data from microcontroller-based IoT devices, Web server-based projects, and so forth

## Slide 42: IoT Software Development (6 of 6)
Figure 13-18 A Raspberry Pi 3B+
youtube.com/watch?v=WEMffdUgWCk
analog life in a digital world

## Slide 43: Knowledge Check Activity 13-2
Which type of device might be used to move a robotic arm up and down?
a. Actuator
b. Servo motor
c. Solenoid
d. PLC

## Slide 44: Knowledge Check Activity 13-2: Answer
Which type of device might be used to move a robotic arm up and down?
Answer: b. Servo motor
Explanation: Servo motors provide either partial rotation (usually about 180 degrees) or continuous 360-degree rotation, and often contain feedback sensors to read the servo’s position. The spindle on a servo motor allows the attachment of an arm that can be used to move objects up and down, left and right, and so forth.

## Slide 45: Self Assessment
Describe some of the IoT devices you have in your home.
What kind of sensor might be used by a controller that’s designed to keep the moisture in the air at a constant level?

## Slide 46: Summary
Now that the lesson has ended, you should be able to:
Define the Internet of Things and list use cases
Describe IoT network technologies
Discuss a variety of IoT devices
Utilize DIY IoT devices